## Slide 1: CLIMSO at Pic du Midi
Laurent Koechlin
IRAP, Université de Toulouse, CNRS

## Slide 2
  The instruments
  Solar survey
  Since 2015: Solar corona with C2
  Space weather
  New developments on C1 and C2
  Data bases
CLIMSO at Pic du Midi

## Slide 3: CLIMSO instruments

## Slide 4: Four solar instruments on the same mount
Two coronagraphs (C1: H-α, C2: He I) and two solar telescopes (L1:H-α, L2: Ca II)

## Slide 5: A fifth instrument for high precision autoguiding
Diffractive imaging: no lens, no mirror, but a binary aperture carved into a copper plate
Image of a
point source
(enlarged)
Image of the Sun
fed to the autoguider
High precision guiding, even if
only part of the Sun is visible.
Above: during a partial eclipse.

## Slide 6
Images from CLIMSO at Pic du Midi :
5 spectral channels sampled
solar spectrum(source :
J.-M. Malherbe web pg
Ca II (393.37 nm)
sampling 1 minute
H-α (656.28 nm)
sampling 1 minute
H-α (656.28 nm)
prominences
sampling 1 minute
He I (1083.0 nm)
prominences
sampling 1 minute
Presently "Service d'observation"
of the French Institut National des Sciences de l'Univers
Fe XIII (1074.7 nm)
CORONA
sampling 30 minutes
I.R.

## Slide 7: Solar survey at Pic du Midi
Since 2007: spectral channels H-α; He I; Ca II
  images: 1 per minute per channel, and the films made from them;
  Field: 1.3 solar diameter, resolution 1 arc second (2048*2048 pixels)
    whole solar disc, prominences, corona
  soon to come: velocimetry, polarisation, magnetic field maps:
    will be presebted by Arturo Lopez Ariste

## Slide 8: Solar survey at Pic du Midi
These data are freely available through various channels
  direct at web page: www.climso.fr
  through VOs : VESPA, EPN-TAP Europlanet
  synergy with MLSO : 12 hours time zone difference

## Slide 9: Solar survey at Pic du Midi
Particularity of CLIMSO compared to other survey facilities:
  Close collaboration with a large group of 90 volonteer astronomers
    financial support from Univ-Toulouse, CNRS, and from a private company
  Over 50/52 weeks covered, weather allowing
  Large direct public audience: 4500 visitors / year in the dome !
    drastic cleaning (dust) constraints !
  and last but not least: Space Weather alert

## Slide 10: Solar survey at Pic du Midi
We calibrate our images of the solar disc in H-α and Ca II:
Emittances in W m^-2 sr^-1, in a plane tangent to the surface of the Sun
The value of a survey is linked to:
Quantity and quality of data:
calibration in physical units, contrast, résolution, regularity of frame rate.
Duration if possible a large number of solar cycles;
Satbility of acquisition conditions: wavelength, spatial and temporal sampling;
Ease of acsess through data bases, free access, no embargo
We will soon calibrate too the images of the prominences in H-α
but we need time to implement this calibration on the He I and Fe XIII channels.

## Slide 11: Films
Disc: H-α
Disc: Ca II

## Slide 12: First images of solar corona
couronne Fer XIII
What is this?
loop
2015-03-20

## Slide 13: Films
Prominences H-α
Corona Fe XIII

## Slide 14
Space weather
The solar disc and prominences are seen in real time by the operators.
they are committed to inform of any large or unusual phenomenon

## Slide 15
Future developments
2016
- renewal of the cameras and acquisition software
2017
- Lucky imaging thanks to the faster cameras
- Synchronous wavelength modulation (Arturo Lopez Ariste)
will improve contrast and allow more observing time at constant weather conditions
- renewed architecture of our data base
- more calibraed channels
- films from the images at "less degraded" resolution

## Slide 16
Future developments
2018, ...
Velocimetry: disk and prominences
  Polarimetry for the Fe XIII or Fe XIV corona images,
  Polarimetry and magnetic fields (talk by by Arturo Lopez Ariste)